| PHYSICAL SPECIFICATION |
| --- |
| Nominal Voltage Nominal Capacity (10HR) | 12V 105Ah |  |
| Dimension | Length Width Container Height Total Height | 507±2mm （19.96inches） 110±2mm (4.33 inches) 223±2mm (8.78 inches) 238±2mm (9.37inches) |  |
| Weight | Approx. 36Kg ( 79.34lbs) |  |
| Standard Terminal | Bolt-and-nut terminal Bolt Type: M6 |  |
| ELECTRICAL SPECIFICATION |
| Characteristics | Discharge curves @ 25℃ (77 °F) |
| Capacity | 20 hour rate (5.25A) 10 hour rate (10.5A) 5hour rate (17.85A) 3hour rate (26.25A) 1hour rate (63A) | 110Ah 105Ah 90Ah 79Ah 63Ah |  |
| Capacity affected by temperature | 40℃ （104 0F） 25℃ （77 0F） 0℃ （32 0F） | 102% 100% 85% |  |
| Internal Resistance | Full charged battery (25℃,77 0F) 4.5mΩ |  |
| Designed life | ≥10 years (25℃,77 0F) |  |
| Constant Voltage Charge | Cycle | Initial Charging Current less than 25A Voltage 14.1~14.4V at 25℃ (77 0F ) Temperature Coefficient –5mV/℃ |  |
|  | Standby | No limit on Initial Charging Current Voltage 13.5~13.8V at 25℃ (77 0F ) Temperature Coefficient –3.3mV/℃ |  |